## Slide 1: Sanitation: Examples of Common Challenges and Deficiencies
Karl Thorson
Food Safety and Sanitation Manager
Sanitation Center of Excellence

## Slide 2: Why Sanitation?
At your table discuss the question:
“Why Focus on Sanitation & Sanitary Design?”
Be prepared to discuss.
Notes: Expected responses
Allergens
Micro
Spoilage
Pathogens
Regulatory compliance
Pest control
Quality
Human safety
Housekeeping
Foreign material
Equipment Reliability

## Slide 3: Benefits Of Sanitation & Sanitary Design
Allergen control
Micro control
Foreign material control
Pest control
Regulatory compliance
Life cycle cost reduction
Quick changeover execution
Product quality
Human safety
Housekeeping
Equipment reliability
Dietary compliance (Kosher, Halal, organic, gluten free)

## Slide 4: Objectives
Communicate the risks being managed
Describe the 6 critical steps in risk management
Identify deficiencies and remediation options
Review case studies
Identify key learnings

## Slide 5: Sanitation Program 6 Critical Steps
  Conduct Needs Analysis
Step 1
  Plan of Action
Step 2
  Validation
Step 3
  Implement Effectively
Step 4
  Document
Step 5
  Verify Effectiveness
Step 6
Determine risks to be managed (allergens, micro, pests, etc)
Effectively reduces/eliminates risks (sanitary design, SSOPs)
Ensure plan addresses specific risks
Communication and training to stakeholders
Defensible plan and records
On-going measures and observations to ensure sustainability
Notes: Slide Title:
Sanitation Basics
Audio / Narration:
(SO_6step-001.wav) A robust sanitation program is comprised of 6 critical steps.
First, we must conduct a needs analysis to understand the reasoning for cleaning and what risks are being managed.
Secondly, we need to put together a plan of action that can be followed and effectively reduces or eliminates any risks.
In step 3, we validate that the plan addresses our specific risks.
Effectively implementing the program by communication and training to all stakeholders, which include those directly involved in the cleaning process as well as those leading sanitation tasks, is step 4.
We also need to make sure we have a defensible plan and that it is appropriately documented.
After the program has been effectively implemented, on-going measures and observations that are as objective as possible must be conducted to verify that the identified needs have been addressed.
Designer Notes:
Developer Notes:
On slide start, fade in title. Sync ‘step’ graphic to come in 1x1 with narration.

## Slide 6: Conduct Needs Analysis
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Assessment
  Chemical
  Physical
  Biological risks
Early Management (EM) focus
  Project success criteria
  Food safety – early & often
Notes: The first step in any sanitation program is to conduct a needs analysis. This process includes assessing physical, chemical, and biological risks within your site, which incorporates the grounds, facilities and equipment.
Early management is key to ensuring success with any project and that food safety is addressed early and often.
Risk assessment is used to identify a threshold at which action needs to be taken to ensure control to an acceptable level

## Slide 7: Risk Criteria
Product design
  RTE (ready to eat) product
  Aw (water activity)
Sanitation practices
  Allergen changeovers
  Cleaning methods
Sanitary design flaws
  Accessibility for cleaning and inspection
Environment
  Pathogens
Notes: Utilize this info to prioritize work and resources (human and $)
No action if accessible and cleanable to a visibly clean standard, control of environmental pathogens, within criteria for indicator microorganisms, no failed results on ingredient or finished product pathogen testing.
Risk grid to define acceptable risk level (severity and likelihood of occurrence)
True risk vs perceived risk (spoilage vs pathogenic organisms)

## Slide 8: Plan of Action
Key Components:
  Sanitary design
  Facility, grounds, equipment cleaning
    Changeover
    Periodic
    Event based
  Cleaning method
    Wet vs. dry
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Notes: Slide Type:
Slide Title:
Audio / Narration:
(QROS6C_step2_01.wav) Step two in the sanitation program is developing a plan of action that addresses and effectively manages the risks identified in step one.
A robust plan of action should include:
Identification of the equipment, area, or utensil to be cleaned or sanitized.
Adequate frequency of sanitation tasks.
Detailed cleaning and sanitizing procedures.
Any necessary chemical information for detergents and sanitizers.
A list of equipment and tools needed to execute the plan.
A breakdown of roles and responsibilities so that staffing needs can be met.
Tools such as SSOPs, OPLs, Maximo and other work instructions can be used to outline how to execute the plan of action.
Designer Notes:
Developer Notes: Title on slide enter, followed by step image fade in. Sync bullets with * & images ^ in narration.

## Slide 9: Allergen Control
  Success criteria: visibly clean, analytical data
Notes: Allergen control
  Design issues preventing access for disassembly, cleaning and inspection to meet acceptable risk criteria (visually clean, anaylical LOD) – enrober, slide gates
  Cleaning method not matching with design
    Sparkle example, pnuetic line s, slide gates, ancchor bearing
  Cleaning method not executed properly
    4X4, no detergent, no mechanical action, wrong or no tools, hot water, correct conc, CIP designed and executed properly
  Poor GMP during cleaning, inspection and reassembly
Micro control
  Poor water management
    Use during full cleaning cycle
    Use during quality changeover or on a low Aw system
    Control of environment
Foreign material control
  Poor execution of sanitation after maintenance or construction work or a contamination event
Pest control
  Poor design to prevent harborage
    Areas left wet and dirty for extended periods of time – drain fly example
    Voids that are difficult to access, clean and inspect – Avon example
  Poor execution of periodic cleaning to prevent infestation
    Lack of deep clean, sheeted down lines, electrical boxes, conduit, etc

## Slide 10: Common Deficiencies – Allergens
Poor sanitary design
  Limited or no access for maintenance, disassembly, cleaning and inspection
Solution
  Utilize sanitary design checklists
    GMA, AMI
    Use 3A, EHEDG, BISSC for proper design

## Slide 11: Poor Sanitary Design - Hidden Spaces

## Slide 12: Poor Sanitary Design – Difficult to Disassemble

## Slide 13: Good Sanitary Design - Tool Free
Principle 3
Notes: Examples of quick release clamps. There are several different styles of quick release clamps.

## Slide 14
Poor Sanitary Design - Hidden Spaces
Notes: The scraper blade shown here was attached with bolts making it difficult to remove and required the use of tools.

## Slide 15: Good Sanitary Design - Tool Free
Notes: In this picture you will see a snap-in snap-out of place scraper blade. The manufacturer of this system shown in the bottom two pictures is manufactured by Kofab.

## Slide 16: Common Deficiencies – Allergens
Cleaning method doesn’t match equipment design
  Wet vs dry cleaning
  Automated cleaning
    CIP – Clean in Place
Solution
  Focus on validating then verifying cleaning procedures

## Slide 17
Poor Sanitary Design – Not CIPable

## Slide 18
Poor Sanitary Design – Not CIPable

## Slide 19
Good Sanitary Design –CIPable

## Slide 20: Sanitary Design Case Study

## Slide 21: Bearing Located at Bottom of Shaft

## Slide 22: Removed Bearing After CIP Cleaning

## Slide 23: Soil Trapped Between Surfaces

## Slide 24: Sanitary Redesign - Final

## Slide 25: Other Options: Eliminate or Clean

## Slide 26: Granola Bar Risk Reduction Case Study

## Slide 27: Risk Assessment
Why did we prioritize granola bars?
  High risk product/process based on the following:
    Allergen
      changeovers
    Micro
      Wet cleaning, RTE, raw ingredients, equipment design
Notes:     Big 8 allergens
    RTE (ready to eat)
      Ambient, shelf-stable, low Aw
      Family & child oriented; includes high-risk groups
    Includes known high-risk micro ingredients – raw agricultural products (primarily Salmonella risk)
    FSMA identified product
    FSMA validation/verification focus
    Post-process risks
      Environment (process contamination) controlled through EMPs, GMPs, and good sanitation.

## Slide 28: Wet/Dry Zoning Conflict

## Slide 29: Wet/Dry Zoning Conflict
Notes: Another example of poor sanitary design “zone control.” The regrind equipment in the back of the picture is a regrinds system for crunchy granola which is a dry system. The equipment in the foreground was design for wet cleaning. The wet washing adds increased challenge and risks to the dry system. Note the high level of humidity suggested by the steam during sanitation.

## Slide 30: Baked Product Cooler
Dry Design + Wet Clean = Micro Risk
Notes: The picture on the right is an interior shot of the cooling tunnel shown on the left.
During a sanitation assessment sanitary design concerns cooling tunnel The cooling tunnel contained heavy condensation within the product contact zone post kill step.
Condensation may have the potential to create ideal micro growth conditions.
Cooling tunnel structural integrity was also determined to possibly contribute to micro risk due to current sanitary design deficiencies.
The cooling tunnel interior and exterior construction primarily consists of fiberglass wrapped around wood framing. Interior and exterior seams are caulked
Doors and section junctions utilize gasket seals
The first step was dehumidifying the air and then switched from wet to dry cleaning. When wet cleaning was being used the system had a 100% failure rate as measured with a indicator organism. When dry cleaning was implemented the system had a 100% approval process with same indicator organisms.

## Slide 31: Condensation – pooling and corrosion

## Slide 32: Poor Sanitary Design – Fiberglass and Wood
Failed caulk seams and exposed wood framing

## Slide 33: Poor Sanitary Design – Hollow Rollers

## Slide 34: Corrective Action Plan
Short Term:
  Re-caulked seams above product zone
  Enhanced environmental sampling
    Confirmed no pathogens

## Slide 35: Environmental Mitigation
Short Term:
  Re-caulked seams above product zone
  Enhanced environmental sampling
    Zone 3 and 4 - Salmonella and Listeria
      All negative

## Slide 36: Corrective Action Plan
Long term:
  Redesigned air handling to ensure dehumidified air
  Replaced ceiling and floor panels
  Converted to dry cleaning
  Micro risk reduced!
    quality indicator organism verification

## Slide 37: Common Deficiencies – Allergens
Cleaning method not executed properly
  Poor SSOP development and execution
    Written procedures do not match on floor activities
    No chemicals or wrong concentration
    Wrong tools for the job
    Limited or no hot water
    CIP not designed and executed properly

## Slide 38: Wet Sanitation Process
Sanitation preparation (disassemble)
Pre-rinse
Wash
  Concentration
  Temperature
  Time
  Mechanical force
Rinse & inspect
  Remove water & assemble
  Pre-operational inspection & verification
Sanitize

## Slide 39: Micro Control
Success criteria: visually clean & quality indicator organisms below defined criteria post sanitation

## Slide 40: Common Deficiencies – Micro Control
Poor water management
  Uncontrolled use for cleaning
    Use during quality changeovers
    Use on low Aw systems
  Control of environment
    Poor ventilation, condensation, leaks
  No wet/dry zoning

## Slide 41: Water Control – Drainage
Principle 3
Notes: Left picture - Poor example of wet sanitation design. The vertical pipe discharges water to the floor increasing micro risk profile.
Right picture - This is an excellent example of a CIP diversion directly to a floor drain. Note that the drain has a physical disconnect to the floor drain to prevent backflow. When engineering a system such as this – you need to make sure that drain capacity is greater than the discharge capability of the CIP to prevent ponding at the floor drain.

## Slide 42: Keys to Success
Good Sanitary Design
Risk Assessment/Management
  Training & Education
  Prioritization processes
Clearly defined success criteria
Robust sanitation programs that are validated, verified and monitored
Special event planning
Visual inspection: it is everyone's best sanitation tool!

## Slide 43: Objectives Met?
Communicate the risks being managed
Describe the 6 critical steps in risk management
Identify deficiencies and remediation options
Review case studies
Identify key learnings

## Slide 44: Thank You! Questions?

## Slide 45: Resources
GMA Sanitary Design Checklists
  Equipment Design Checklist for Low Moisture Foods
  Facility Design Checklist

## Slide 46: Poor Sanitary Design – Wet/Dry Interface

## Slide 47: Poor Sanitary Design – Wet/Dry Interface

## Slide 48: New Sanitary Design

## Slide 49: Physical Hazard: Foreign Material Control
Goal: No plastic, wood, metal, glass, or other misc. contaminates in and around the product zone
  Success criteria – absence via visual inspection

## Slide 50: Common Deficiencies – Foreign Material Control
Poor sanitation
  Following maintenance repairs
  During and after construction work
  After a contamination event
Notes: Allergens
Micro
Spoilage
Pathogens
Regulatory compliance

## Slide 51: Swarf
  Grindings: the fine metallic shavings removed by grinding or cutting tools

## Slide 52: Pest Control
Goal: No pest infestation on the property and no pest activity in the facility
  Success criteria – absence via visual inspection

## Slide 53: Common Deficiencies – Pest Control
Poor design to prevent harborage
  Voids difficult to access, clean and inspect
Lack of deep cleaning
  Wet, dirty stagnate areas
Notes: Allergens
Micro
Spoilage
Pathogens
Regulatory compliance

## Slide 54: Periodic Clean – Remove Soil & Water